| Job Safety Analysis Sheet |
| --- |
| JOB DESCRIPTION: Gas Welding | JSA Ref. No. JSA / KOC / 08 |
| Facility: | Work Area / Equipment: | Permit No. Date: |
| PERSONAL PROTECTIVE EQUIPMENT & TOOLS: Hard Hat, Safety Shoes, Apron, Welding Hood, Safety Goggles, Hand Gloves, Multi Gas Detector, |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | Yes /No | PRECAUTIONS |
| Planning | Presence of flammable / toxic Vapor or Liquid |  | Ensure the worksite is free from flammable / toxic vapor or liquid by safe preparation (isolation, depressurizing, draining, venting, flushing, purging as required) |
|  | Fire & Explosion |  | The entry of non – certified equipment (Gas Cylinder Banks, Crane, Vehicles etc) to be authorized under Permit to Work System. Keep the fire extinguishers & fire hoses in ready condition. |
|  | Non – compliance of KOC F & S Regulations and HSE MS Procedure |  | Refer Chapter -16 KOC F& S Regulations, HSEMS Procedures - Doc. No. SA.KOC.021 ‘Welding & Cutting’; Doc. No. SA.KOC.004 “Permit to Work”. |
|  | Unintended Shutdown of Facility / Equipment |  | Identify the safety override required for the work. |
|  | Unauthorized Work |  | Take a Hot Work Permit and other associated permits from Asset Owner. |
| Cutting / Welding | Defective Tools |  | Ensure the gas cutting equipment (blowpipe, hoses, oxy-acetylene cylinders, pressure gauge) are free from defect . |
|  | Radiation from Welding Flame / Rays (Flash Eye) |  | Wear protective goggles & Clothing. |
|  | Exposure to Welding Fumes |  | Ensure proper ventilation and fume extraction equipment in case of welding inside an enclosure |
|  | Burns |  | Wear long sleeved coverall, leather apron; welder’s hood. |
|  | Falling of Sparks |  | Enclose the welding area through tarpaulin. |
|  | Flash Back Fire |  | Provide a check valve (flash back arrester) between oxy-acetylene hose & gas regulator. |
|  | Argon Cylinder near the Hot Work area |  | Keep oxy – acetylene cylinders at least 5 meters away from hot work area. Isolate the cylinder when not in use. |
| Windup & Housekeeping | Scattered Material |  | Ensure proper wind up & housekeeping at worksite. The accessories (regulator, blowpipe, hose, isolation valve, gauge) not being used must be disconnected from gas cylinder and stored separately. |
| Additional Hazards (Other than indicated above) |  |  |
| JSA Done By | Name: Designation: KOC / ID. No. Company: Controlling Team: Contract No.(If Applicable): Signature: Date: |